## Slide 1: Turtle bot nano V2.0
Kent State University

## Slide 2: Turtle bot Nano
V2.0

## Slide 3: PCB Schematics

## Slide 4: PCB Design

## Slide 5
Component name | Configuration | Test Example | note
Led (3) | Led1-16 Led2-17 Led3-18 | Example 1 | 
Switch (4) | SW1-22 SW2-21 SW3-19 SW4-0 | Example 2 | 
Servo (4) | Servo 1 - GPIO 2 Servo 2 - GPIO 3 Servo 3 - GPIO 6 Servo 4 - GPIO 7 | Example 3 | 
IR (2) | IR1 – GPIO-26 IR2 – GPIO-27 | Example 4 | 
Motor Driver (1) | rightMotorE1 = 8; rightMotorE2 = 9; leftMotorE1 = 14; leftMotorE2 = 15; rightMotorINT1 = 10; rightMotorINT2 = 11; leftMotorINT1 = 12; leftMotorINT2 = 13; |  | 
OLED (1) | SDA – GPIO 4, SCL – GPIO 5 | Example 6 | Internally connected
IMU (1) | SDA – GPIO 4, SCL – GPIO 5 |  | Internally connected
Lidar | PWM – GPIO 28, Tx/Rx – GPIO 1 |  | 
Charging status | Blue light charging, Red means Full charged | Switch OFF { keep charge} | 

## Slide 6
Test Example | note
Example 1 | 
Example 2 | 
Example 3 | 
Example 4 | 
Example 5 | 
Example 6 | 
Example 7 | 
Example 8 | 

## Slide 7: Arduino Setup

## Slide 8: PIN DIAGRAM

## Slide 9: Coding using Arduino IDE

## Slide 10: Programming

## Slide 11: If serial port issues: FILE -> Preference and select Additional board manager URLs: paste the URL https://github.com/earlephilhower/arduino-pico/releases/download/global/package_rp2040_index.json Install new Board: Board manager -> PICO -> Raspberry Pi Pico/RP2040

## Slide 12: Programming for new Boards “Board 2”

## Slide 13: Coding
Turtle Bot Nano – Version 2.0

## Slide 14: EXAMPLE 1
On Board Led Test
const int led1 = 16; // led 1
const int led2 = 17; // led 2
const int led3 = 18; // led 3
void setup() {
// Initialize LED pins as outputs
pinMode(led1, OUTPUT);
pinMode(led2, OUTPUT);
pinMode(led3, OUTPUT);
}
//The loop function runs over and over again forever
void loop() {
digitalWrite(led, HIGH); delay(1000); digitalWrite(led1, LOW); delay(1000);
digitalWrite(led2, HIGH); delay(1000); digitalWrite(led2, LOW); delay(1000);
digitalWrite(led3, HIGH); delay(1000); digitalWrite(led3, LOW); delay(1000);
}

## Slide 15: EXAMPLE 2
On Board Button Test
< Single button>
const int SWPin1 = 22;
const int SWPin2 = 21;
const int SWPin3 = 19;
const int SWPin4 = 0;
const int SWPin = 22; // change the Switch number
const int ledPin1 = 16;
const int ledPin2 = 17;
const int ledPin3 = 18;
int SW = 0; // value read from the switch
int count = 0; // LED state counter
void setup() {
Serial.begin(9600);
pinMode(SWPin, INPUT_PULLUP); // Using INPUT_PULLUP to enable internal pull-up resistor
pinMode(ledPin1, OUTPUT);
pinMode(ledPin2, OUTPUT);
pinMode(ledPin3, OUTPUT);
}
void loop() {
SW = digitalRead(SWPin);
// If the switch is pressed (LOW state), increment the count
if (SW == LOW) {
count++;
delay(200); // Debounce delay
}
// Set the LED states based on the count
if (count == 1) {
digitalWrite(ledPin1, HIGH); digitalWrite(ledPin2, LOW); digitalWrite(ledPin3, LOW);
} else if (count == 2) {
digitalWrite(ledPin1, LOW); digitalWrite(ledPin2, HIGH); digitalWrite(ledPin3, LOW);
} else if (count == 3) {
digitalWrite(ledPin1, LOW); digitalWrite(ledPin2, LOW); digitalWrite(ledPin3, HIGH);
} else if (count == 4) {
// Reset count to 0 and turn off all LEDs
count = 0;
digitalWrite(ledPin1, LOW); digitalWrite(ledPin2, LOW); digitalWrite(ledPin3, LOW);
}
// Print the switch state and count to the Serial Monitor
Serial.print("\tSW = ");
Serial.print(SW);
Serial.print("\tCount = ");
Serial.println(count);
delay(200);
}

## Slide 16: EXAMPLE 3
On Board Servos Test
#include <Servo.h>
//Servo pins
Servo servo1;
Servo servo2;
Servo servo3;
Servo servo4;
int pos = 0; // variable to store the servo position
void setup() {
servo1.attach(2); // Attach servo 1 to GPIO pin 2
servo2.attach(3); // Attach servo 2 to GPIO pin 3
servo3.attach(6); // Attach servo 3 to GPIO pin 6
servo4.attach(7); // Attach servo 4 to GPIO pin 7
}
void loop() {
for (pos = 0; pos <= 180; pos += 1) {servo1.write(pos); delay(15);}for (pos = 180; pos >= 0; pos -= 1) {servo1.write(pos); delay(15);}
for (pos = 0; pos <= 180; pos += 1) {servo2.write(pos); delay(15);}for (pos = 180; pos >= 0; pos -= 1) {servo2.write(pos); delay(15);}
for (pos = 0; pos <= 180; pos += 1) {servo3.write(pos); delay(15);}for (pos = 180; pos >= 0; pos -= 1) {servo3.write(pos); delay(15);}
for (pos = 0; pos <= 180; pos += 1) {servo4.write(pos); delay(15);}for (pos = 180; pos >= 0; pos -= 1) {servo4.write(pos); delay(15);}
}

## Slide 17: EXAMPLE 4
On Board IR module Test
// IR sensor pins
const int irSensor1 = A0; // Analog pin 0 (pin 26)
const int irSensor2 = A1; // Analog pin 1 (pin 27)
void setup() {
Serial.begin(9600); // setup serial
// Initialize IR sensor pins as inputs
pinMode(irSensor1, INPUT);
pinMode(irSensor2, INPUT);
}
void loop() {
int irValue1 = analogRead(irSensor1); Serial.print(“Ir1 Value = ” ); Serial.print(irValue1); Serial.print(“/t” );
int irValue2 = analogRead(irSensor2); Serial.print(“Ir2 Value = ” ); Serial.print(irValue2); Serial.print(“/n” );
}

## Slide 18: Scanner
#include <Wire.h>
// Set I2C bus to use: Wire, Wire1, etc.
#define WIRE Wire
void setup() {
WIRE.begin();
Serial.begin(9600);
while (!Serial)
delay(10);
Serial.println("\nI2C Scanner");
}
void loop() {
byte error, address;
int nDevices;
Serial.println("Scanning...");
nDevices = 0;
for(address = 1; address < 127; address++ )
{
// The i2c_scanner uses the return value of
// the Write.endTransmisstion to see if
// a device did acknowledge to the address.
WIRE.beginTransmission(address);
error = WIRE.endTransmission();
if (error == 0)
{
Serial.print("I2C device found at address 0x");
if (address<16)
Serial.print("0");
Serial.print(address,HEX);
Serial.println(" !");
nDevices++;
}
else if (error==4)
{
Serial.print("Unknown error at address 0x");
if (address<16)
Serial.print("0");
Serial.println(address,HEX);
}
}
if (nDevices == 0)
Serial.println("No I2C devices found\n");
else
Serial.println("done\n");
delay(5000); // wait 5 seconds for next scan
}
EXAMPLE 5
On Board, OLED and IMU Test

## Slide 19: OLED AND IMU

## Slide 20: PICO – OLED libraries

## Slide 21
#include <Arduino.h>
#include <U8g2lib.h>
#include <Wire.h>
U8G2_SSD1306_128X64_NONAME_F_HW_I2C u8g2(U8G2_R2, /* reset=*/ U8X8_PIN_NONE);
void setup(void) {
u8g2.begin();
}
void loop(void) {
u8g2.clearBuffer();
u8g2.setFont(u8g2_font_ncenB08_tr);
u8g2.drawStr(0, 20, "ATR lab");
u8g2.sendBuffer();
}
EXAMPLE 6
On Board OLED Test

## Slide 22: UDP – Server/Client

## Slide 23: Use the “Board 2” – for more info | Slide 11

## Slide 24: UDP – Server/Client
Server – Turtle bot Nano
Use the Wifi/ Hotspot
Show Turtle bot IP address
Perform the Client actions
Wifi
< Mobile Hotspot > Connected Using
Hotspot name: *****
Password: *******
Client – Keyboard
Connect to Turtle Bot IP address
Send Commands to trigger the actions

## Slide 25
UDP – Server(pico) and client(pc)
#include <WiFi.h>
#include <WiFiUdp.h>
// Replace these with your WiFi network settings
const char* ssid = "SHIELD";
const char* password = "AVENGERS";
WiFiUDP udp;
const unsigned int localPort = 8888; // Local port to listen on
void setup() {
Serial.begin(115200);
// Connect to WiFi
WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) {
delay(500);
Serial.print(".");
}
Serial.println("WiFi connected");
Serial.print("IP address: ");
Serial.println(WiFi.localIP());
// Start UDP
udp.begin(localPort);
Serial.print("UDP server started on port ");
Serial.println(localPort);
}
void loop() {
int packetSize = udp.parsePacket();
if (packetSize) {
// Received a packet
Serial.print("Received packet of size ");
Serial.println(packetSize);
Serial.print("From ");
IPAddress remoteIp = udp.remoteIP();
for (int i = 0; i < 4; i++) {
Serial.print(remoteIp[i], DEC);
if (i < 3) {
Serial.print(".");
}
}
Serial.print(", port ");
Serial.println(udp.remotePort());
// Read the packet into a string
String incomingPacket = "";
while (udp.available()) {
incomingPacket += (char)udp.read();
}
Serial.print("Contents: ");
Serial.println(incomingPacket);
}
}
Upload the code into pico
Run the python code using terminal
import socket
# Server IP and Port
server_ip = "192.168.252.124" # Replace PICO_IP_ADDRESS with the actual IP address of your Pico
server_port = 8888
# Create a UDP socket
client_socket = socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
# Timeout for receiving the response (optional)
client_socket.settimeout(1)
try:
while True:
# Get user input from the keyboard ('1', '2', '3', '4')
message = input("Enter your message ('1', '2', '3', '4'): ")
if message in ['1', '2', '3', '4']:
# Send the message to the server
client_socket.sendto(message.encode(), (server_ip, server_port))
print(f"Sent '{message}' to the server.")
else:
print("Please enter only '1', '2', '3', or '4'.")
except KeyboardInterrupt:
print("Program exited.")
finally:
client_socket.close()

## Slide 26
UDP – Server(pico) and client(pc) <keeping led and oled> <led on as output>
Upload the code into pico
Run the python code using the terminal – code in slide 25
#include <WiFi.h>
#include <WiFiUdp.h>
#include <U8g2lib.h>
#include <Wire.h>
// WiFi network settings
const char* ssid = "SHIELD";
const char* password = "AVENGERS";
WiFiUDP udp;
const unsigned int localPort = 8888; // Local port to listen for UDP messages
// OLED display setup
U8G2_SSD1306_128X64_NONAME_F_HW_I2C u8g2(U8G2_R0, U8X8_PIN_NONE);
// GPIO pins for the LEDs
const int ledPins[4] = {16, 17, 18, 19};
void setup() {
Serial.begin(115200);
// Connect to WiFi
WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) {
delay(500);
Serial.print(".");
}
Serial.println("\nWiFi connected");
Serial.print("IP address: ");
Serial.println(WiFi.localIP());
// Start the UDP server
udp.begin(localPort);
Serial.print("UDP server started on port ");
Serial.println(localPort);
// Initialize the OLED display
u8g2.begin();
// Test display message
u8g2.clearBuffer();
u8g2.setFont(u8g2_font_ncenB08_tr);
u8g2.drawStr(0, 20, "Startup OK");
u8g2.sendBuffer();
delay(2000); // Show the message for 2 seconds
// Initialize LED pins
for (int i = 0; i < 4; i++) {
pinMode(ledPins[i], OUTPUT);
digitalWrite(ledPins[i], LOW); // Ensure all LEDs are off initially
}
}
void loop() {
int packetSize = udp.parsePacket();
if (packetSize) {
// Read the incoming packet
String incomingPacket = "";
int len = udp.read((unsigned char*)incomingPacket.begin(), 255);
if (len > 0) incomingPacket[len] = 0;
Serial.print("Received packet of size ");
Serial.println(packetSize);
Serial.print("Contents: ");
Serial.println(incomingPacket);
// Process the incoming message
if (incomingPacket >= "1" && incomingPacket <= "4") {
int ledNumber = incomingPacket.toInt() - 1;
// Turn off all LEDs
for (int i = 0; i < 4; i++) {
digitalWrite(ledPins[i], LOW);
}
// Turn on the selected LED
digitalWrite(ledPins[ledNumber], HIGH);
// Update the OLED display
u8g2.clearBuffer();
u8g2.setFont(u8g2_font_ncenB08_tr);
String message = "LED " + incomingPacket + " ON";
u8g2.drawStr(0, 20, message.c_str());
u8g2.sendBuffer();
// Print to Serial Monitor
Serial.println(message);
}
}
}

## Slide 27
UDP – Server(pico) and client(pc) <leds with their number>
Upload the code into pico
Run the python code using the terminal – code in slide 25
void loop() {
int packetSize = udp.parsePacket();
if (packetSize) {
// Read the incoming packet
char incomingPacket[255]; // Make sure the buffer is large enough
int len = udp.read((unsigned char*)incomingPacket, 255);
if (len > 0) incomingPacket[len] = 0; // Null-terminate the string
Serial.print("Received packet of size ");
Serial.println(packetSize);
Serial.print("Contents: ");
Serial.println(incomingPacket);
// Process the incoming message
if (incomingPacket[0] >= '1' && incomingPacket[0] <= '4') {
int ledNumber = incomingPacket[0] - '0' - 1;
// Turn off all LEDs
for (int i = 0; i < 4; i++) {
digitalWrite(ledPins[i], LOW);
}
// Turn on the selected LED
digitalWrite(ledPins[ledNumber], HIGH);
// Update the OLED display
u8g2.clearBuffer();
u8g2.setFont(u8g2_font_ncenB08_tr);
char message[20];
sprintf(message, "LED %d ON", ledNumber + 1); // Format the message with LED number
u8g2.drawStr(0, 20, message);
u8g2.sendBuffer();
// Print to Serial Monitor
Serial.println(message);
}
}
}
#include <WiFi.h>
#include <WiFiUdp.h>
#include <U8g2lib.h>
#include <Wire.h>
// WiFi network settings
const char* ssid = "SHIELD";
const char* password = "AVENGERS";
WiFiUDP udp;
const unsigned int localPort = 8888; // Local port to listen for UDP messages
// OLED display setup
U8G2_SSD1306_128X64_NONAME_F_HW_I2C u8g2(U8G2_R0, U8X8_PIN_NONE);
// GPIO pins for the LEDs
const int ledPins[4] = {16, 17, 18, 19};
void setup() {
Serial.begin(115200);
// Connect to WiFi
WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) {
delay(500);
Serial.print(".");
}
Serial.println("\nWiFi connected");
Serial.print("IP address: ");
Serial.println(WiFi.localIP());
// Start the UDP server
udp.begin(localPort);
Serial.print("UDP server started on port ");
Serial.println(localPort);
// Initialize the OLED display
u8g2.begin();
// Test display message
u8g2.clearBuffer();
u8g2.setFont(u8g2_font_ncenB08_tr);
u8g2.drawStr(0, 20, "Startup OK");
u8g2.sendBuffer();
delay(2000); // Show the message for 2 seconds
// Initialize LED pins
for (int i = 0; i < 4; i++) {
pinMode(ledPins[i], OUTPUT);
digitalWrite(ledPins[i], LOW); // Ensure all LEDs are off initially
}
}

## Slide 28
UDP – Server(pico) and client(pc) full code
Upload the code into pico
#include <WiFi.h>
#include <Arduino.h>
#include <WiFiUdp.h>
#include <U8g2lib.h>
#include <Wire.h> // Motor pins
const int rightMotorE1 = 8;
const int rightMotorE2 = 9;
const int leftMotorE1 = 14;
const int leftMotorE2 = 15;
const int rightMotorINT1 = 10;
const int rightMotorINT2 = 11;
const int leftMotorINT1 = 12;
const int leftMotorINT2 = 13; // WiFi network settings
const char* ssid = "SHIELD";
const char* password = "AVENGERS"; WiFiUDP udp;
const unsigned int localPort = 8888; // Local port to listen for UDP messages // OLED display setup
U8G2_SSD1306_128X64_NONAME_F_HW_I2C u8g2(U8G2_R0, U8X8_PIN_NONE); // GPIO pins for the LEDs
const int ledPins[4] = {16, 17, 18, 19}; void setup() {
Serial.begin(115200); // Set motor pins as outputs
pinMode(rightMotorE1, OUTPUT);
pinMode(rightMotorE2, OUTPUT);
pinMode(leftMotorE1, OUTPUT);
pinMode(leftMotorE2, OUTPUT);
pinMode(rightMotorINT1, OUTPUT);
pinMode(rightMotorINT2, OUTPUT);
pinMode(leftMotorINT1, OUTPUT);
pinMode(leftMotorINT2, OUTPUT); // Connect to WiFi
WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) {
delay(500);
Serial.print(".");
}
Serial.println("\nWiFi connected");
Serial.print("IP address: ");
Serial.println(WiFi.localIP()); // Start the UDP server
udp.begin(localPort);
Serial.print("UDP server started on port ");
Serial.println(localPort); // Initialize the OLED display
u8g2.begin(); // Test display message
u8g2.clearBuffer();
u8g2.setFont(u8g2_font_ncenB08_tr);
u8g2.drawStr(0, 20, "Startup OK");
u8g2.sendBuffer();
delay(2000); // Show the message for 2 seconds
// Initialize LED pins
for (int i = 0; i < 4; i++) {
pinMode(ledPins[i], OUTPUT);
digitalWrite(ledPins[i], LOW); // Ensure all LEDs are off initially
}
}
void loop() {
int packetSize = udp.parsePacket();
if (packetSize) {
char incomingPacket[255]; // Buffer for incoming packet
int len = udp.read((unsigned char*)incomingPacket, 255);
if (len > 0) incomingPacket[len] = 0; // Null-terminate the string
Serial.print("Received packet of size ");
Serial.println(packetSize);
Serial.print("Contents: ");
Serial.println(incomingPacket);
// Initial motor stop state
stopMotors();
// Process the incoming message for motor control
switch (incomingPacket[0]) {
case '1': // Forward
driveForward();
break;
case '2': // Backward
driveBackward();
break;
case '3': // Left
turnLeft();
break;
case '4': // Right
turnRight();
break;
}
// Update OLED display
updateOLED(incomingPacket[0]);
// Print action to Serial Monitor
Serial.printf("Action: %c\n", incomingPacket[0]);
}
}
void driveForward() {
digitalWrite(rightMotorINT1, HIGH);
digitalWrite(rightMotorINT2, LOW);
digitalWrite(leftMotorINT1, HIGH);
digitalWrite(leftMotorINT2, LOW);
}
void driveBackward() {
digitalWrite(rightMotorINT1, LOW);
digitalWrite(rightMotorINT2, HIGH);
digitalWrite(leftMotorINT1, LOW);
digitalWrite(leftMotorINT2, HIGH);
}
void turnLeft() {
digitalWrite(rightMotorINT1, HIGH);
digitalWrite(rightMotorINT2, LOW);
digitalWrite(leftMotorINT1, LOW);
digitalWrite(leftMotorINT2, HIGH); // Adjust as needed for your motor configuration
}
void turnRight() {
digitalWrite(rightMotorINT1, LOW);
digitalWrite(rightMotorINT2, HIGH);
digitalWrite(leftMotorINT1, HIGH);
digitalWrite(leftMotorINT2, LOW); // Adjust as needed for your motor configuration
}
void stopMotors() {
digitalWrite(rightMotorINT1, LOW);
digitalWrite(rightMotorINT2, LOW);
digitalWrite(leftMotorINT1, LOW);
digitalWrite(leftMotorINT2, LOW);
}
void updateOLED(char command) {
char message[20];
switch (command) {
case '1':
sprintf(message, "Moving Forward");
break;
case '2':
sprintf(message, "Moving Backward");
break;
case '3':
sprintf(message, "Turning Left");
break;
case '4':
sprintf(message, "Turning Right");
break;
default:
sprintf(message, "Stopped");
break;
}
u8g2.clearBuffer();
u8g2.setFont(u8g2_font_ncenB08_tr);
u8g2.drawStr(0, 20, message);
u8g2.sendBuffer();
}
Client code in slide 25

## Slide 29
Line Following robot – Narrow stright line following
#include <Arduino.h>
#include <U8g2lib.h>
#include <Wire.h>
#include <Adafruit_MPU6050.h>
#include <Adafruit_Sensor.h>
#include <Servo.h>
// OLED setup
U8G2_SSD1306_128X64_NONAME_F_HW_I2C u8g2(U8G2_R2, /* reset=*/ U8X8_PIN_NONE);
// Motor control pins
const int rightMotorE1 = 8; // GP8
const int rightMotorE2 = 9; // GP9
const int leftMotorE1 = 14; // GP14
const int leftMotorE2 = 15; // GP15
const int rightMotorINT1 = 10; // GP10
const int rightMotorINT2 = 11; // GP11
const int leftMotorINT1 = 12; // GP12
const int leftMotorINT2 = 13; // GP13
const int led1 = 16; // led 1
const int led2 = 17; // led 2
const int led3 = 18; // led 3
// IR sensor pins
const int irSensor1 = A0; // Analog pin 0 (pin 26)
const int irSensor2 = A1; // Analog pin 1 (pin 27)
Adafruit_MPU6050 mpu;
void setup() {
// Initialize motor control pins as outputs
pinMode(rightMotorE1, INPUT);
pinMode(rightMotorE2, INPUT);
pinMode(leftMotorE1, INPUT);
pinMode(leftMotorE2, INPUT);
pinMode(rightMotorINT1, OUTPUT);
pinMode(rightMotorINT2, OUTPUT);
pinMode(leftMotorINT1, OUTPUT);
pinMode(leftMotorINT2, OUTPUT);
// Initialize LED pins as outputs
pinMode(led1, OUTPUT);
pinMode(led2, OUTPUT);
pinMode(led3, OUTPUT);
// Initialize IR sensor pins as inputs
pinMode(irSensor1, INPUT);
pinMode(irSensor2, INPUT);
// Initialize OLED
u8g2.begin();
// Initialize IMU
Serial.begin(115200);
while (!Serial) delay(10); // will pause Zero, Leonardo, etc until serial console opens
Serial.println("Adafruit MPU6050 test!");
if (!mpu.begin()) {
Serial.println("Failed to find MPU6050 chip");
while (1) delay(10);
}
Serial.println("MPU6050 Found!");
mpu.setAccelerometerRange(MPU6050_RANGE_8_G);
mpu.setGyroRange(MPU6050_RANGE_500_DEG);
mpu.setFilterBandwidth(MPU6050_BAND_21_HZ);
Serial.println("");
delay(100);
}
void loop() {
// Read IR sensors
int irValue1 = analogRead(irSensor1);
int irValue2 = analogRead(irSensor2);
// Display IR values for debugging every 500ms
static unsigned long lastDisplayTime = 0;
if (millis() - lastDisplayTime > 500) {
displayIRValues(irValue1, irValue2);
lastDisplayTime = millis();
}
// Determine motor actions based on IR sensor values
int error = irValue1 - irValue2;
if (irValue1 > 400 || irValue2 > 400) {
// Proportional control for smoother turns
int baseSpeed = 255; // Maximum speed
int turnSpeed = constrain(abs(error), 0, baseSpeed);
if (error > 0) {
// Turn left
analogWrite(rightMotorINT1, baseSpeed - turnSpeed);
analogWrite(rightMotorINT2, LOW);
analogWrite(leftMotorINT1, LOW);
analogWrite(leftMotorINT2, turnSpeed);
} else if (error < 0) {
// Turn right
analogWrite(rightMotorINT1, LOW);
analogWrite(rightMotorINT2, turnSpeed);
analogWrite(leftMotorINT1, baseSpeed - turnSpeed);
analogWrite(leftMotorINT2, LOW);
} else {
// Move forward
analogWrite(rightMotorINT1, baseSpeed);
analogWrite(rightMotorINT2, LOW);
analogWrite(leftMotorINT1, baseSpeed);
analogWrite(leftMotorINT2, LOW);
}
} else {
// Both sensors on white surface, stop
stopMotors();
}
delay(5); // Short delay for sensor stability
}
void moveForward() {
digitalWrite(rightMotorINT1, LOW);
digitalWrite(rightMotorINT2, HIGH);
digitalWrite(leftMotorINT1, HIGH);
digitalWrite(leftMotorINT2, LOW);
}
void moveBackward() {
digitalWrite(rightMotorINT1, HIGH);
digitalWrite(rightMotorINT2, LOW);
digitalWrite(leftMotorINT1, LOW);
digitalWrite(leftMotorINT2, HIGH);
}
void turnRight() {
digitalWrite(rightMotorINT1, HIGH);
digitalWrite(rightMotorINT2, LOW);
digitalWrite(leftMotorINT1, HIGH);
digitalWrite(leftMotorINT2, LOW);
}
void turnLeft() {
digitalWrite(rightMotorINT1, LOW);
digitalWrite(rightMotorINT2, HIGH);
digitalWrite(leftMotorINT1, LOW);
digitalWrite(leftMotorINT2, HIGH);
}
void stopMotors() {
digitalWrite(rightMotorINT1, LOW);
digitalWrite(rightMotorINT2, LOW);
digitalWrite(leftMotorINT1, LOW);
digitalWrite(leftMotorINT2, LOW);
}
void displayMessage(const char *message) {
u8g2.clearBuffer();
u8g2.setFont(u8g2_font_ncenB08_tr);
u8g2.drawStr(0, 20, message);
u8g2.sendBuffer();
}
void ledTest() {
displayMessage("testing led 1"); delay(100); digitalWrite(led1, HIGH); delay(1000); digitalWrite(led1, LOW); delay(1000);
displayMessage("testing led 2"); delay(100);digitalWrite(led2, HIGH); delay(1000); digitalWrite(led2, LOW); delay(1000);
displayMessage("testing led 3"); delay(100);digitalWrite(led3, HIGH); delay(1000); digitalWrite(led3, LOW); delay(1000);
}
void imuTest() {
sensors_event_t a, g, temp;
mpu.getEvent(&a, &g, &temp);
u8g2.clearBuffer();
u8g2.setFont(u8g2_font_ncenB08_tr);
u8g2.setCursor(0, 10);
u8g2.print("Accel X,Y,Z: ");
u8g2.print(a.acceleration.x);
u8g2.print(",");
u8g2.print(a.acceleration.y);
u8g2.print(",");
u8g2.print(a.acceleration.z);
u8g2.setCursor(0, 20);
u8g2.print("Gyro X,Y,Z: ");
u8g2.print(g.gyro.x);
u8g2.print(",");
u8g2.print(g.gyro.y);
u8g2.print(",");
u8g2.print(g.gyro.z);
u8g2.sendBuffer();
}
void displayIRValues(int value1, int value2) {
u8g2.clearBuffer();
u8g2.setFont(u8g2_font_ncenB08_tr);
u8g2.setCursor(0, 10);
u8g2.print("IR Sensor 1: ");
u8g2.print(value1);
u8g2.setCursor(0, 20);
u8g2.print("IR Sensor 2: ");
u8g2.print(value2);
u8g2.sendBuffer();
}

## Slide 30
THANK YOU